## Slide 1
Simulation Proposal for New International Arrivals

## Slide 2
Understanding the Brief
Objective
To build a simulation of the newly proposed international arrivals layout to help the projects team visualise passenger flow, identify the bottlenecks and to validate the design decisions before construction of the International arrivals begins.
Validate Design
Test the newly proposed layout against current demand patterns and passenger behaviours
Identify Bottlenecks
Pinpoint where the queues, congestion and delays are likely to occur under peak/off peak conditions
Inform Decisions
Provide evidences to support or refine the design before capital investment

## Slide 3
Assumptions to Gather
Part 1: Demand, Service Times & Physical Constraints
Demand ( Who is arriving and when?)
International flight schedule
Peak hour arrivals, aircraft types (A380 vs 737 = very different pax volumes), seasonal variation
Seat load factors & nationality mix
Determines e gates vs manned desk vs special assistance routing for each flight
Contact stand vs remote stand split
Remote stands trigger coach transfers (96 pax batch for 1 bus) vs continuous airbridge flow or via steps
Coach frequency from remote stands
Controls the arrival pulse timing 96 pax from 1 Bus or more buses hitting immigration hall at once
Processing Times at Immigration Hall ( How fast is each step?)
E-gate cycle time
Eligible Biometric Passports (Biometric scan + e-gates open/close will typically take under 60 seconds per passenger?
Manned desk time by passport type
Non-EU (3–4min), Eligible Passport with Visas needs stamping
Special assistance lane service time
PRM’s, Unaccompanied Minors escort handoff + processing will take longer per pax, do we have dedicated lane capacity?
First bag / last bag delivery curves
Time from aircraft arrival to first bag on belt and gap to last bag will vary depending by the aircraft type
Infrastructure & Capacity (What are the physical limits?)
Number of e gates & manned desks
The new layout doesn’t specify the actual numbers, this directly sets passport control throughput capacity
Queue space in a lane
What would be the Physical limit before overflow this will be critical for safety regulations
Belt capacity & allocation rules
Which flights will go to which belt? Can multiple run simultaneously? What would be the changeover time?
Walking distances between zones
Entry → immigration → Baggage reclaim → Customs → exit in metres this would convert to travel time in the model

## Slide 4
Assumptions to Gather
Part 2: Passenger Behaviour & Disruption Scenarios
Passenger Behaviour & Routing (How do passengers choose and move?)
E-gates vs. manned desk eligible %
Driven by nationality mix but eligible passports with visas must use manned desks despite biometric e gates eligibility
PRM (WCHC,WCHS,WCHR) % per flight
PRMs disembark first via ambulift at remote stands, escorted directly to special assistance lane a completely separate flow path
Family or group queueing behaviour
Does groups queue together at one desk or split across channels? Affects processing batch sizes
Trolley collection rate & exit dwell
What % collect a £1 trolley? Trolley parking is far left in the layout cross flow of passenger movement might affect congestion
Disruptions & Variability (What goes wrong and how often?)
Ramp staff shortage frequency & duration
Delays baggage offload start by 10–30+ min due to staff shortage in that case, passengers will clear immigration but bags aren’t there, causing crowding at baggae reclaim
Wind speed threshold & annual frequency
High winds prevent cargo door opening which will affect ALL flights during event window, not just one
Aircraft trim delay (older aircraft types)
Bags cannot be offloaded until all passengers disembark on certain aircraft adds 10–20 min to first bag time
Belt congestion from overlapping flights
If previous flight bags uncollected, next flight’s bags queue at offload position which will delay further and crowding
Deeper scrutiny / secondary referral rate
2–5% of passengers may be referred for additional checks that creates extra dwell at manned desks
If e-gates goes down, what would be the fallback process for eligible passports pax
E-gate malfunction or system outage frequency
Airbridge / Stand door malfunction
If door between airbridge/steps malfunctions and fails to open pax will be held at the bridge until it gets resolved and they reach the immigration. Whats the fallback or how redirection to another entry point happens

## Slide 5
Key Questions to ask for data collection
Seven teams will feed inputs into our simulation, each one owns a piece of the model we cannot build without.
Simulation
Model Input
Project Team
Design capacity, success criteria, layout variants
Operations / Dispatch
Stand allocation, ramp delays, wind thresholds, coach ops
Passenger Service Front House
Deplaning times, door malfunctions, family behaviour
Border Force
Processing times, e-gates outages, Eligible Passport but with visas needs stamping
Special Assistance
Agent capacity, ambulift process, PRM escort times
Airside / Baggage
First/last bag times, belt allocation, trim offload delays
Business Analytics
Historical flight data, passenger flow data, processing time distributions, weather records
Detailed questions per team on following slides →

## Slide 6
Key Questions for Data Collection and Prep in Detail
Part 1: Ground Operations, Passenger Handling & Infrastructure
Project Team
What is the design hour capacity this layout must handle?
What are the success criteria for our layout like the max queue time, throughput space utilisation?
Are there any alternative layouts or phases to test in simulation?
What is the target journey time from entry to landside exit?
Is there a budget for additional infrastructure if simulation shows shortfalls?
Operations / Dispatch
What is the contact stand vs. remote stand split for international flights?
How frequently do ramp staff shortages occur and what’s the typical delay?
What wind speed threshold stops cargo door ops? How many days/yr
Which aircraft types have trim constraints on baggage offload?
What is the coach turnaround cycle like the load, transit, unload, return time?
Passenger Service / Front House
What is typical deplaning time for a full narrow-body vs. wide-body aircraft?
What’s the fallback process when an airbridge or stand entry door malfunctions?
Do families and groups typically stay together or split at immigration lanes?
How many passenger service agents are available on shift at peak times?
What is the process for handling CTA passengers
Airside Operations / Baggage
What is the avg time from aircraft arrival to first bag on belt? And last bag?
How is belt allocation decided — by flight, by gate, by time, or manually?
What happens when a belt is still occupied by a previous flight’s bags?
How much extra time does trim-constrained offload add to bag delivery?
What is the baggage trailer transit time from remote stands to reclaim?

## Slide 7
Key Questions for Data Collection and Prep in Detail
Part 2: Border Control, Special Assistance & Data Availability
Border Force
What are current avg processing times at e gates vs manned desks by passport type?
What nationalities are e gate eligible and what are the exceptions (like Tier 5 visa)?
What is the deeper scrutiny / secondary referral rate and average duration?
How often do e gate system outages occur? What’s the fallback protocol?
What % of passengers currently use e-gates vs. manned desks?
How is the special assistance lane staffed dedicated officer or shared?
Special Assistance Team
How many assistance agents are available per shift? Max simultaneous PRMs?
What is the avg escort time: aircraft to immigration (airbridge vs. ambulift)?
How long does the ambulift process take setup, loading, drive to terminal?
What happens when multiple PRM flights arrive at once ambulift queue?
How many ambulifts are available at
Do unaccompanied minors follow the same special assistance flow?
Business Analytics Team
Business Analytics Team
What historical flight schedule data is available (AODB, OAG) and how far back does it go?
Do we have passenger flow data from existing terminals like sensors, Wi-Fi tracking, CCTV counts?
Are there existing processing time distributions to calibrate e gate and manned desk service times?
Is there historical baggage delivery time data (first bag / last bag) by aircraft type?
Do we have weather disruption records we can correlate with ramp delay data?

## Slide 8
My Layout :
Landside arrivals area for passengers
Airside (staff only area)
Entry to hall (Walk-ins)
Entry to hall (From Coaches)
▼
▼
New immigration hall
Long Serpentine queue marshalling with rope and stanchion
Eligible Passports queue
All other Passports queue
PRM/UM/Disability queue
▼
▼
▼
Passport control (e-gates)
eligible biometric passports
Passport control (manned)
All other passports + Eligible passports that needs stamping
Special assistance Manned Desk
PRM + escorts
Digital signage on the ceiling that can show the routing guidance for passengers
▼
▼
▼
PRM (WCHC/WCHS) escort
via ambulift from aircraft stand
▼
Baggage reclaim hall
Reclaim Belt 1
Reclaim Belt 2
Reclaim Belt 3 (flexible only during peak times)
Trolley parking
Baggage
offload
positions
▼
Exit baggage reclaim
Staff guiding pax
Buffer zone between the passport control and baggage reclaim

## Slide 9
Why this could matter for a reliable simulation :
Change
Original layout
Improved layout
Simulation impact
Three immigration lanes instead of two
Two types: E-gates and manned desks
Three lanes: E-gates, manned desks and special assistance (PRM/UM) desk.
This Enables accurate routing logic, passengers split across three channels each with different processing times
Serpentine queue with staff directed split
No queue management shown
Shared serpentine entry that splits into e gate and manned queues with staff directing passengers at the decision point
Allows modelling of dynamic queue behaviour so staff can redirect passengers to balance load across lanes in real time
PRM escort route from airside
No PRM flow shown
Dedicated dashed route from airside via ambulift directly into the special assistance desk or also for PRM pax assisted with escorts via jetbridge would no need to be crossing other flows
PRM passengers are a separate entity type with their own resource agents, ambulifts
Buffer zone between immigration and reclaim
Single narrow corridor labelled 'To baggage reclaim'
Dedicated transition zone that absorbs surges when all three lanes release passengers simultaneously
Prevents the bottleneck that the simulation would otherwise flag at the immigration to the reclaim transition
Third flexible reclaim belt
Two fixed belts
Two permanent belts plus a third flex belt will be activated during the peak especially during summer time or when one becomes faulty
Enables scenario testing simulation can compare 2belt vs 3 belt performance during peak demand
Digital signage for real time routing
No passenger guidance system
Ceiling mounted displays showing live wait times per lane and guiding the passengers to the right queues
Changes queue selection logic from fixed probability to dynamic and passengers choose based on displayed wait times
Staff guiding passengers at queue split
No staff or guidance shown in the layout
Staff positioned at the end of serpentine split point to direct passengers to the correct lane based on Nationality or passport type
Enables dynamic queue balancing in the model staff can redistribute passengers across lanes based on real time queue lengths

## Slide 10
Simulation Approach ( Passenger Flow Paths )
Three distinct passenger journeys through the system from aircraft to exit
Standard passenger (airbridge)
Aircraft at
contact stand
▶
Airbridge
▶
Walk in
entry
▶
Serpentine
queue
▶
Staff directs
to lane (E-gate/Manned Desk)
▶
Passport
control
▶
Buffer
zone
▶
Baggage
reclaim
▶
Exit
Coach passenger (remote stand)
Aircraft at
remote stand
▶
Coach transfer
(96 batch for 1 bus
>96 2nd bus)
▶
Coach
drop off at Immigration Hall Entry
▶
Serpentine
queue
▶
Staff directs
to lane
(E-gate/Manned Desk)
▶
Passport
control
▶
Buffer
zone
▶
Baggage
reclaim
▶
Exit
PRM / UM / Special assistance
Disembark
first
▶
Ambulift or
escort
▶
Bypass
queue
▶
Special
assist Manned desk
▶
Escorted to
reclaim
▶
Collect bags
(escorted)
▶
Escorted
to exit

## Slide 11
Simulation Approach (Agent Entity Attributes)
Each virtual passenger(Agent) in the model carries these properties which determines the routing and the timings
These attributes are assigned to each passenger entity when they are generated in the model based on flight schedule data and probability distributions gathered from the stakeholder team.
Attribute
Values
Impact on simulation
Arrival mode
Walk in via airbridge or coached from remote stand (batch of 96 for 1Bus)
continuous trickle vs pulse arrival
Flight number
Links passenger to a specific flight in the schedule
Connects to aircraft type stand allocation and bag delivery timing
Nationality / passport
Determines which passport control lane the passenger is routed to
Mobility
Standard or PRM (reduced mobility)
PRM passengers follow a completely separate flow with escort and ambulift
UM status
Unaccompanied minor yes or no
Routes through special assistance flow with dedicated escort
Group type
Solo traveller, family or a tour group
Affects queue behaviour and groups may process as a batch at one desk
Bag count
0, 1, or 2+ checked bags
Determines how long the passenger stays at the baggage belt

## Slide 12
Simulation Approach ( Conditions & Decision Logic )
The routing rules, processing times and disruption scenarios applied at each decision point in the model
Routing conditions ( where does each passenger go?)
At entry
If arrival mode = coach → enter as batch of 96 for 1 bus with transit delay.
If walk-in → continuous trickle from airbridge
Queue split
Staff directs the pax from serpentine queue based on passport→ e-gate lane.
Non-EU or Visa stamping needed→ manned desk lane
PRM routing
If mobility = PRM or UM = yes → bypass serpentine entirely escorted directly to special assistance manned desk from airside
Belt allocation
Flight number → belt mapping rule.
If allocated belt full → overflow to flex Belt 3 (if peak activated)
Exit decision
If trolley needed (probability based on bag count) → add trolley collection time, otherwise walk directly to exit
Processing times (how long does each step take?)
E-gate
Stochastic triangular distribution: min ~25 sec, mode ~45 sec, max ~70 sec per passenger
Manned desk
Varies by passport type
Special assistance
PRM/UM processing ~4-5 mins including escort handoff and document check
Baggage delivery
First bag: 15–25 min after aircraft arrival. Last bag: 25–45 min. Varies by aircraft type and delay conditions
Disruption conditions (what triggers delays in the model?)
Ramp staff shortage
Probability event → offload delayed 10–30+ min
Passengers clear immigration but bags aren’t there → reclaim crowding
High winds
If wind speed exceeds threshold → ALL flights’ baggage offload paused for event duration → system wide congestion
Aircraft trim
If aircraft type = older model → offload waits until last passenger disembarks.
Adds 10–20 min to first bag time
Belt congestion
If belt still occupied by previous flight → new flight bags queue at offload position until space clears
E-gate outage
If e gates go down → ALL egates eligible passengers redirect to manned desks → manned queue surges instantly
Door malfunction
If airbridge/stand door fails → passengers held at aircraft until resolved. Entire flight delayed entering system
Coach delay
If no coach/ no availability of steps due to demand for a remote stand flight → passengers held on aircraft until a coach/steps is dispatched. Delays entry into the immigration hall by the coach wait time compressing the arrival pulse

## Slide 13
What the Simulation Will Deliver
The key performance indicators I will track and the outputs that the project team will receive
Key performance indicators
Queue wait time
Average and max wait at serpentine queue and each passport control lane processing
Hall occupancy
Peak passenger count in immigration hall vs. fire safety capacity limit
Journey time
End to end time from entry to exit for each passenger type
Bag wait time
Time passengers wait at belt for first bag by flight and aircraft type
Bottleneck detection
Which process point fails first under peak demand and at what threshold
Scenario comparison
2 belts vs 3 staffing levels, egate outage impact, peak vs offpeak
What the project team receives
Working simulation model
A calibrated model of the new international arrivals layout that can be reused for future scenario testing and layout changes
Results report with visualisations
A clear report covering KPI outputs with different visualisations showing congestion points, queue profiles over time, peak vs off peak comparison
Recommendations for the project team
Evidence based suggestions on infrastructure sizing staffing levels and layout refinements supported by the simulation data

## Slide 14
Estimated Time to Complete Simulation & Deliver Insights
Data Gathering &
Stakeholder Consultation
8–10 hrs
Stakeholder meetings with all seven teams identified in this proposal. Collect flight schedules, processing time data, staffing levels, disruption frequency, infrastructure specifications
Data Cleaning,
Validation & Preparation
6–8 hrs
Clean and format collected data into simulation ready inputs.
Build flight schedule profiles and define probability distributions for processing times and set up passenger attribute logic.
Model Build
in AirTOP/CAST
15–20 hrs
Constructing the layout:
Immigration hall with three passport control lanes, serpentine queue, buffer zone, baggage reclaim with three belts
Define all passenger flow paths, routing conditions, entity attributes.
Calibration
& Validation
5–8 hrs
Running model against known scenarios. Comparing outputs with real world observations. Tune parameters.
Scenario Testing
& Analysis
8–10 hrs
Execute all 7 scenarios. Capture KPIs. Identify patterns, bottlenecks design sensitivities.
Insight Generation
& Presentation
5–8 hrs
Analyse the results, produce visualisations (heatmaps, queue profiles, journey time charts) and write the results report with bottleneck findings
Prepare recommendations for the project team
Total Estimated Effort: ~50–60 hours (7–8 working days) depending on the data availability and stakeholder response times.
Timelines may also vary if additional scenarios or layout variants are requested

## Slide 15
Thank You